## Slide 1: Unit 3: Cadaster survey

## Slide 2: Structure and function of cadaster & land registration system

## Slide 3: Structure and function
Land is defined as an area of the surface of the earth together with the water, soil, rocks, minerals and hydrocarbons beneath or upon it and the air above it.
Land in relation to land registration and cadastre and in general to land information systems to which category land registration and cadastre belong, concerns
  abstract or thematic attributes (legal status, value, tax data)
  physical, spatial or topographic ones (location, dimensions, area, use).

## Slide 4: Structure and function
Land registration is a process of official recording of rights in land through deeds or as title on properties.
  an official record (land register) of rights on land or of deeds concerning changes in the legal situation of defined units of land.
  gives an answer to the questions who and how.
Cadaster is a methodically arranged public inventory of data concerning properties within a certain administration (e.g. city), based on a survey of their boundaries.
  gives an answer to the question where and how much.
Notes: Cadaster is a methodically arranged public inventory of data concerning properties within a certain administration (e.g. city), based on a survey of their boundaries. Such properties are systematically identified by means of some separate designation. The outlines of the property and the parcel identifier normally are shown on large-scale maps which, together with registers, may show for each separate property the nature, size, value and legal rights associated with the parcel. It gives an answer to the question where and how much.

## Slide 5: Structure and function
Land registration and cadastre
  usually complement each other, they operate as interactive systems.
The land registration answers the questions as to who and how.
The cadastre answers the questions as to where and how much.
Notes: Land registration and cadaster: Land registration and cadastre usually complement each other, they operate as interactive systems. Land registration puts in principle the accent on the relation subject-right, whereas cadastre puts the accent on the relation on right-object. In other words: the land registration answers the questions as to who and how, the cadastre answers the questions as to where how much.
Because land registration and cadastre (who and how along with where and how much) complement each other, the terms "land recording" or "land records" are usually used to indicate that these two components belong together as a whole.

## Slide 7: Cadastral survey definition
The international association of geodesists (FIG) statement on the cadastre states that a cadastre is normally a parcel based, and up-to-date land information system containing a record of interests in land (e.g. rights, restrictions and responsibilities).
It usually includes a geometric description of land parcels linked to other records describing the nature of the interests, the ownership or control of those interests, and often the value of the parcel and its improvements.
It may be established for fiscal purposes (e.g. valuation and equitable taxation), legal purposes (conveyancing), to assist in the management of land and land use (e.g. for planning and other administrative purposes), and enables sustainable development and environmental protection.

## Slide 8: Cadastre
The Cadastre is a land information system, usually managed by one or more government agencies.
The Cadastre was designed to assist in land taxation, real estate conveyancing, and land redistribution.
The Cadastre helps to provide those involved in land transactions with relevant information and helps to improve the efficiency of those transactions and security of tenure in general.
It provides governments at all levels with complete inventories of land holdings for taxation and regulation. But today, the information is also increasingly used by both private and public sectors in land development, urban and rural planning, land management, and environmental monitoring.

## Slide 9: Cadastre
A Cadastre is normally a parcel-based system, i.e. information is geographically referenced to unique, well-defined units of land.
These units are defined by the formal or informal boundaries marking the extent of lands held for exclusive use by individuals and specific groups of individuals (e.g. families, corporations, and communal groups).
Each parcel is given a unique code or parcel identifier. Examples of these codes include addresses, co-ordinates, or lot numbers shown on a survey plan or map.

## Slide 10: Cadastral maps
Graphical indices of these parcels, known as cadastral maps, show the relative location of all parcels in a given region/ administration.
Cadastral maps commonly range from scales of 1:10,000 to 1:500.
Large scale diagrams or maps showing more precise parcel dimensions and features (e.g. buildings, irrigation units, etc.) can be compiled for each parcel based on ground surveys or remote sensing and aerial photography.
Information in the textual or attribute files of the Cadastre, such as land value, ownership, or use, can be accessed by the unique parcel codes shown on the cadastral map, thus creating a complete Cadastre.

## Slide 11: The base data required in any public land information system
The Cadastre forms part of the base data required in any public land information system.
Since information about land parcels and land holdings is often needed by many different users, having a unified, standard Cadastre for each jurisdiction helps to avoid duplication and assists in the efficient exchange of information.
The Cadastre is usually created and managed through a government organisation.

## Slide 12: Examples of the data of general interest to a wide user community
Examples of the data of general interest to a wide user community, that is usually considered part of the Cadastre, include:
  Land parcels (e.g. Location, boundaries, co-ordinates)
  Land tenure (e.g. Property rights, ownership, leases)
  Land value (e.g. Quality, economic value, tax value, value of improvements)

## Slide 13: E.g. of information can also be connected to land parcels
Other information can also be connected to land parcels through the unique parcel identifiers and through cadastral index maps.
Such information may be of importance to specific user groups and includes:
  Buildings and other improvements
  Agricultural data (land capability classifications, land use)
  Forestry data
  Utilities (e.g. Water, electricity, communications)
  Fisheries (noting individuals holding rights in inland and coastal waters)
  Environmental quality (particularly for site-specific analysis and monitoring)
  Demography (population statistics, consumer marketing data, etc.)

## Slide 14: Well organized cadastral system is helpful in
Facilitating efficient and safe land transaction;
Providing security and protection to owners/holders of parcels, which in turn facilitates investment and associated banking services like loans and mortgage;
Minimizing disputes of land- related issues by assuring legal rights of owners over their plots;
Serving as a tool for assessing and levying land- related taxes;
Providing the necessary information for planning purposes;
Managing environmental issues;
Facilitating the implementation of land reform when necessary.
Registering and carrying out inventory of heritages which are found in urban centers; and
Registering tourist facilities and thereby promoting the tourist industry.
Notes: Providing the necessary information for planning purposes so that all stakeholders who may involve in infrastructure development or similar other development issues could carry out their respective duties in a coordinated manner. This in turn helps avoid duplication of efforts and hence waste of resource;

## Slide 15: Summary
Generally, cadastre is an important management tool that helps wisely utilize resources of urban centers.
This on the other hand enables municipalities to properly handle all issues related to their respective urban areas, which of course is a means to effectively discharge responsibilities by maintaining good urban governance.
Thus, all municipalities and pertinent organizations are advised to have an up- to-date land register (cadastre) system so as to efficiently manage their respective urban centers and institutions.
Cadastral surveys are surveys whose aim is to demarcate or create, measure, define, describe and record the position of boundary land as property.
Their ultimate purpose being to give unambiguous, graphical, numerical or descriptive information relating to location, extent, shape and size of land parcels. Such information is vital in the support of a register of titles for land ownership and transfer of rights in land.

## Slide 17: Demarcation, and delineation of boundaries and parcels
The basic spatial unit in a Cadastre is known as a parcel.
A parcel can be defined in many ways depending on the purpose of the Cadastre.
In some systems, a property may consist of several parcels of land which may be distributed over a small region such as a village.
The flexibility in the definition makes it possible to adapt the cadastral system to particular needs and thus also adapt the cost of the registration.
If, for instance, the purpose is mainly to protect the ongoing traditional land use, larger parcels representing common interests can be defined as the basis for the system.
Notes: A parcel can be defined in many ways depending on the purpose of the Cadastre. For instance, an area with a particular type of land use may be considered as a parcel in some systems; in others it is defined as an area exclusively controlled or owned by an individual or group of individuals (e.g. family or corporation).

## Slide 18: Boundary ?
Boundary in general terms defined as the extreme limit of something.
As for land parcel, a boundary may be defined as the line, alone or together with others, which encloses or defines the limits of the land parcel.
The word limit here has a divisive connotation as it divides between one land parcel and another.
Such limits may be described in terms of numerical data, (such as bearings and distances or coordinate value), in which case this give rise to fixed boundaries e.g. boundaries that are numerically described.
These limits may also be described by the location of a physical feature, (such as river, a ditch, a road, and a mountain range) on the ground.

## Slide 19: Boundary ?
Boundaries of parcels can be defined by physical demarcation on the ground or by a mathematical description usually based on a co-ordinate system.
The accuracy and cost of cadastral surveys is dependent on the accuracy needed for boundary descriptions.
The accuracy should reflect factors such as the value of the land, the risk and cost of land disputes and the information needs of the users of the cadastre.

## Slide 20: Boundary ?
Most parcel boundaries are defined by stable marks or visible features on the ground, which can be natural or artificial.
They can be represented by lines on maps, often described by bearings or azimuths and distances, or by coordinates.
If the representation on the map has legal priority over the marks on the ground in cases of dispute, the demands for survey accuracy are usually higher than if the case is the opposite.

## Slide 21: Types of boundaries
Physical demarcation on the ground is important because it provides actual notice of the boundaries to the landowners.
Basically, there are two types of boundaries:
  general and
  fixed boundaries.

## Slide 22: General Boundary
General boundary is one whose position is not usually determined. For this reason, such a boundary is said to be indeterminate or indefinite.
A boundary of this type may be marked by some physical feature such as stream, a wall and a hedge or its position may be described relative to features such as wall, a road, a stream etc. and the boundary may be unmarked.
The use of general boundaries relies heavily on a number of things including the existence of a physical feature on the ground and permanence of such a feature with lapse of time. Lost boundaries can be a source of headache to re-establish, particularly where the boundaries including all neighboring reference objects and features have been destroyed.

## Slide 23: Fixed Boundary
Fixed boundary is a boundary line whose precise position has been created or determined and recorded by a survey operation.
It make use of markers which are emplaced on the ground and are defined in accordance with specified accuracies that will enable individual land parcels so surveyed to be readily and reliably identified or relocated.
Such boundaries are usually linked to framework of horizontal geodetic control established over a country.
Because coordinates are ultimately, or can be, computed for the boundary markers, the name coordinated boundary is often used for fixed boundaries.

## Slide 24: Demarcation and delineation
The demarcation and delineation of the boundaries are a part of a cadastral survey aimed at defining the parcel on the ground and securing evidence for the re-establishment of the boundary if it disappears.
As the costs of cadastral surveys are relatively high, the technical requirements of demarcation and delineation (e.g. accuracy and survey methodology) should reflect such factors as the value of the land, the risk of land disputes and information needs of the users of the Cadastre.

## Slide 25: Types of cadaster

## Slide 26: Types of Cadastre
Cadastres may be classified in many ways, e.g. by:
  Primary function (e.g. Supporting taxation, conveyancing, land distribution, or multipurpose land management activities);
  The types of rights recorded (e.g. Private ownership, use rights, mineral leases);
  The degree of state responsibility in ensuring the accuracy and reliability of the data (e.g. Complete state mandate, shared public and private responsibility); 1st, 2nd level certficate
  Location and jurisdiction (e.g. Urban and rural cadastres; centralised and decentralised cadastres);

## Slide 27: Other factors that will influence the format and management of the Cadastre include
history, culture, and traditional land tenure arrangements;
area;
physical and economic geography;
population distribution;
level of technology;
traditional public administration arrangements;
land and property law arrangements;
land policy priorities for the jurisdiction.

## Slide 28: Modern land information systems
One major consequence of the development of modern land information systems using computer technology has been the creation of closer coordination among organisations responsible for parts of the Cadastral data.

## Slide 29: Types of cadastre
In general, cadastre can be classified into three categories based on their use, type, quality and quantity of data summarized in it.
Accordingly, the three types of cadastre are:
  fiscal,
  legal and
  multi-purpose.
The purpose of these various types of cadastres vary depending on their specific nature.

## Slide 30: Fiscal cadastre
It records information for the purpose of property valuation and land taxation.
Here, the basic information needed is location and value of the parcel.
In this regard, there must be some sort of agreed upon valuation method that help determine the value of a parcel.

## Slide 31: Legal cadastre
It is a register aiming at identifying the legal owner and exact boundaries of the parcel.
To establish legal cadastre it requires delineation of boundaries of the given parcel through surveying and mapping and thereby provision of legal rights. In this respect, legal cadastre is helpful in:
  Defining property rights;
  Describing the extent of property rights;
  Supporting land transfer; and
  Providing evidence of ownership.

## Slide 32: Multi-purpose cadaster
It is a relatively new approach of land information system which is reported to have been introduced after the Second World War.
This land register system incorporates all the necessary information, at one source, which among others are information related to legal and fiscal cadastre, land use, buildings, infrastructures of underground and overhead constructions, soil and other aspects of the given parcel.
In many respects, multi-purpose cadastre seems to be an important type of land information system for it provides multitudes of information related to a given parcel.

## Slide 33: Questions:
Give short, brief and precise answer for the following questions.
  1) Explain the concept of cadastre and its importance.
  2) What is cadastral surveying?
  3) What is parcel and parcel boundary.
  4) Discuss the types of parcel boundary and compare each other.
  5) Describe the types of cadastre and their main purpose

## Slide 34: Survey of public lands, boundary surveys

## Slide 35: Data capturing techniques for cadaster
Rural
  Spatial data capturing techniques for land registration
  Capturing non-spatial data
Urban
  Spatial data capturing techniques for land registration
  Capturing non-spatial data
Students are advised to refer to existing guidelines and directives for the urban and rural cadaster