## Slide 1: GIS part Urban Cadastral Surveying and Mapping
Practical on Urban cadaster

## Slide 2: GIS data organization
Recap
(shapefile and Geodatabase)

## Slide 3: A database
Spatial (Geographic) database is simply databases containing geographic data for a particular area and subject or a collection of spatial data that acts as a model of reality.
Cadaster database ?
GIS data organization

## Slide 4: GIS File Data Formats
In the GIS world, there are many different GIS file formats.
For this training/sector, we will focus on:
  shapefiles for vector data,
  imagine and GeoTiff files for rasters and
  file geodatabases for both vector and raster data.
GIS data organization

## Slide 5: Vector Data File Formats Shapefile
A shapefile is a file-based data format native to ArcView 3.x software.
A shapefile is a feature class–it stores a collection of features that have the same geometry type (point, line, or polygon), the same attributes, and a common spatial extent.
A “single” shapefile is actually composed of at least three files, and as many as eight.
Each file that makes up a “shapefile” has a common filename but different extension type.
GIS data organization

## Slide 6: files that define a “shapefile”
File extension | Content
.dbf | Attribute information
.shp | Feature geometry
.shx | Feature geometry index
.aih | Attribute index
.ain | Attribute index
.prj | Coordinate system information
.sbn | Spatial index file
.sbx | Spatial index file
Note that each file has a specific role in defining a shapefile.
E.g.
Kebele.dbf
Kebele.shp
Kebele.shx
Kebele.prj
GIS data organization

## Slide 7: File Geodatabase
A file geodatabase is a relational database storage format.
It’s a far more complex data structure than the shapefile and consists of a .gdb folder housing dozens of files.
GIS data organization

## Slide 8
Sample content of an ArcGIS file geodatabase
!

## Slide 9
GIS data organization

## Slide 10: Sample content of an ArcGIS file geodatabase
GIS data organization

## Slide 11: Data quality
An error is something you have done that is considered to be incorrect or wrong, or that should not have been done.
Error can be related with
  Attribute, and/or
  Location
Errors created by faulty processing.
Errors created by human error.
Errors from obvious sources (e.g. incomplete maps)
Errors created during data input (e.g. digitizing).
Errors created by map projection.
GIS data organization

## Slide 13: Managing GIS Files
Unless you are intimately familiar with the file structure of a GIS file, it is best to copy/move/delete GIS files from within the software environment.
ArcCatalog (part of the ArcGIS suite) acts like a Windows file management environment with the added benefit that it recognizes GIS files.

## Slide 14: ArcCatalog
The ArcCatalog application provides a catalog window that is used to organize and manage various types of geographic information for ArcGIS for Desktop

## Slide 15: ArcCatalog is used to organized & managed
Geodatabases
Raster files
Map documents, layer files
Geoprocessing toolboxes
And much more
Notes: The kinds of information that can be organized and managed in ArcCatalog
Geodatabases
Raster files
Map documents, globe documents, 3D scene documents, and layer files
Geoprocessing toolboxes, models, and Python scripts
GIS services published using ArcGIS for Server
Standards-based metadata for these GIS information items
And much more

## Slide 16: ArcCatalog is used to
Organize your GIS contents
Manage geodatabase schemas
Search for and add content to ArcGIS applications
Document your contents
Manage GIS servers
Manage standards-based metadata

## Slide 17: ArcMap
is the main component of Esri's ArcGIS suite of geospatial processing programs,
is used primarily to view, edit, create, and analyze geospatial data.
allows the user to explore data within a data set, symbolize features accordingly, and create maps.

## Slide 18: Practical with the GIS software
Getting started with ArcCatalog in focus with exploring existing cadastral data
Getting started with ArcMap Interface for displaying and interacting with existing cadastral features (orthophoto and vector features)
Exploring and understanding GIS data organization using shape file and geodatabase approach
Working with file geodatabase (feature dataset, feature class, topology, advanced editing, …)

## Slide 20: Getting started with ArcCatalog
in focus with exploring existing cadastral data
Page 68 - 72
!

## Slide 21: Working with ArcCatalogue
ArcCatalogue
  Start
  GUI = Graphic User Interface
Connect to folder (workspace)
Explore and preview data
  Metadata
  Spatial data
  Attribute data
Disconnect folder
+

## Slide 22: Structure of the file geodatabase
+

## Slide 23
GIS data organization
+

## Slide 24: Existing data organization
+

## Slide 25: Subfolders
+

## Slide 26: Sample cadaster database feature dataset
+

## Slide 27: Sample cadaster database feature dataset feature class

## Slide 28: Working with ArcMap - start
ArcMap
  Start
  GUI = Graphic User Interface
Connect to folder (workspace)
Check the contents of the
  folders / databases
+

## Slide 29: Working with ArcMap – Add data
Add data/file
Table of content management
  View data
  Change order
Use toolbars / buttons
  Zoom in / zoom out/ pan
Open table of a layer and preview the contents
Select / deselect (layer / attribute)
+

## Slide 30: Working with ArcMap – project
Project
  Save
  Close
  Restart
+

## Slide 31: Working with ArcMap – new project
Project – new
Connect folder from catalogue in ArcMap
Check the contents of folders and database
Add selected layers: raster, vector
Properties of a layer
Change symbol of a layer
Save project
+

## Slide 32: Working with ArcMap – toolbars / panels
Toolbars
Panels
Close unnecessary toolbars/panels
Change position of toolbars
Arrange the toolbars properly
+

## Slide 34: Getting started with ArcMap
Interface for displaying and interacting with existing cadastral features (orthophoto and vector features)
!

## Slide 35: Urban Legal Cadastre Standard
No. – 03/2015 Addis Ababa

## Slide 36: Cadastral Data Standard (see chapter Two of Urban Legal Cadastre Standard , No. – 03/2015 , Addis Ababa)
For preparing a cadastre base map, only the following data sources shall be used (the spatial component (parcel map) of the data should be obtained using the following techniques)
  Ground surveying
  Aerial photography
  High resolution satellite imagery (Refer to Urban Cadastral Surveying Directive article 37 (6))

## Slide 37: Cadastral Data Standard (see chapter Two of Urban Legal Cadastre Standard , No. – 03/2015 , Addis Ababa)
For preparing a cadastre base map, only the following data sources shall be used (The non-spatial (descriptive) information should be obtained from):
    Existing Legal Documents
    Field Observation
    Other Data Sources

## Slide 38: Cadastral Data Standard (see chapter Two of Urban Legal Cadastre Standard , No. – 03/2015 , Addis Ababa)
The following data can also be useful in preparing cadastral maps:
  Local development plan (LDP)
  Survey Plans
  Existing base maps

## Slide 39: Feature Extraction
When ortho-photo is used as data source in preparing cadastral map, the feature extraction method must be primarily using photogrammetric technique (stereo compilation method).
But as an option, on-screen/heads-up digitizing can also be used provided that the capture scale is kept constant at scale of 1:500 for 1:2000 scale output.

## Slide 40: Feature Extraction
While digitizing a parcel boundary from aerial photograph, centerline of a boundary/fence should be used whenever the sharing is between two adjacent private landholding of a parcel.
On the other hand, whenever the sharing of boundaries is with road and open public land or easement, the outer part of the boundary/fence outline shall be used.

## Slide 41: Feature Extraction
Filed boundary conformation is mandatory for each parcel boundary after on-screen digitization.
Vertex should be available only at corner points of a parcel boundary where it changes its direction.
Avoid unnecessary vertex during digitization.

## Slide 42: Feature Extraction
Each parcel boundary should be a closed polygon.
An entire area of a town/a project area should be covered by a parcel map including
  road, streams, gullies, hills, pocket areas etc.
Not copy / paste instead merge the parcels
  ???

## Slide 43: Feature Extraction
Thus an aggregate area of each parcels of a town should be equal to a total area of that town.

## Slide 45: Datum and Map Projection System
Based on the national standard adopted by EMA, coordinates shall be calculated in reference to the grid on UTM projection and zones 36, 37, or 38 depending on the geographic location.
  Projection – Universal Transverse Mercator
  Spheroid/Reference Ellipsoid – Clarke1880 modified
  Local Geodetic Datum – Adindan
  Unit – Meter

## Slide 46: Datum and Map Projection System
Projection Parameters
  UTM Grid Zone – 36, 37, 38 depending up on the geographic location
  Central Meridian – 33°E for zone 36; 39° E for zone 37; and 45° E for zone 38 3)
  False Easting – 500,000 m E
  False Northing – 0 m N
  Scale Factor - 0.9996

## Slide 47: Coordinate Transformation Parameters and Coordinate System
The datum transformation parameters provided by EMA shall be used for transforming the geodetic coordinates from WGS84 to Adindan geodetic datum.
In cadastral surveying and mapping activities the transformed coordinates shall be stated in Cartesian coordinate system;
  The parameters to be used are:-
  Semi-major axis (a): 6378249.145metre
  Semi-minor axis (b): 6356514.9667metre
  Ellipsoidal flattening (f):1/293.466307656

## Slide 48: Coordinate Transformation Parameters and Coordinate System
Translational transformation parameters are:-
  Δx = -162
  Δy = -12
  Δz = 206

## Slide 49: Non spatial data
!

## Slide 50: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Uniqueness -is the most important attribute of a PIN. It refers to a one-to -one relationship between a parcel and its identifier. An identifier should be assigned to one and only one parcel.

## Slide 51: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Permanent- Parcel identifiers should be permanent and change only when absolutely necessary. This is especially important when stakeholders such as planning departments or tax payment tracking services link their own databases to the assessor's.

## Slide 52: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Simple- Parcel identifiers should be easy to understand and use quarter-quarter-section numbers, along with individual parcel and have as few digits as possible. A parcel identifier that is uncomplicated and easily understood helps to reduce errors in its use.

## Slide 53: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Easily Maintainable- The parcel identification system should be easy to maintain and should efficiently accommodate changes, such as splitting or merging parcels.

## Slide 54: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Flexible -The parcel identification system should be reasonably flexible. It should be capable of serving a variety of uses:
  not just land parcels, but
  multi-story condominiums,
  sub-surface rights, leases, easements, and so on.

## Slide 55: Unique Parcel identification code Standard (Basic Principles)
The parcel identification code shall meet the following principles:
Accessibility - the description about the parcel shall be accessible to the user.
  Relate / join with other table such as register

## Slide 56: Unique Parcel identification code Standard (Assigning Parcel Identification Code)
According to Urban Landholding Registration Proclamation No. 818/2014 Article 8, each parcel shall have a unique parcel identification code which may not be duplicated on another parcel in any urban center. For this purpose a national standard is required to assign a code for each parcel.

## Slide 57: Unique Parcel identification code Standard (Assigning Parcel Identification Code)
The unique parcel identification code shall take the following form:
Region code + city/town code + + Woreda code + Neighborhood code City block number + parcel number
  Region code (type= Alphabetic;2 digit)
  City/Town code (type= number;3 digits)
  Woreda / kebele (type= number; 2 digits)
  Neighborhood (type= number; 2 digits)
  City Block number code (type = number ; 2digit)
  Parcel number code (type = number; 3 digit)
Total No. of digits:- 14

## Slide 58: Unique Parcel identification code Standard (Assigning Parcel Identification Code)
Example:
  OR001062314112
  Oromiya region, Adama town, Woreda 06, Neighborhood 23, city block 14 & parcel no. 112

## Slide 59: Unique Parcel identification code Standard
City/Town code: The town or city code shall be assigned by regional government urban bureau.
Condominium/Apartment code: Specific condominium units and house number should be assigned separately once the parcel (condominium site) is identified.
  Thus, it is easily possible to identify by indexing the condominium to the ground parcel.

## Slide 60: Unique Parcel identification code Standard
The index should take the following code:
Condominium Block unit code (type= number; 2 digit)
Condominium floor code (type= number; 2 digit)
House number code (type= number; 2 digit)
Example: OR001062314112050201=20 digits

## Slide 61: Control of New Parcel Numbers
The control of the subsequent allocation, re-allocation, and withdrawal of parcel identifiers is part of the larger process of managing land-tenure changes.
There are various techniques available for monitoring the fidelity of a parcel identifier from the time of its initial assignment through subsequent processing, most of which employ the addition of a redundant check digit.
The simplest approach is the addition of a check digit at the end of an identifier, which is mathematically related to the sequence of digits in the identifier.

## Slide 62: Splitting a parcel
If the configuration of a parcel is changed (e.g., typically by subdivision), that parcel ceases to exist, and new identifiers are assigned to the new parcels following the last parcel in the block.
However, the original parcel remains as a historic entity and the descriptions of it that were entered in the various registers and files when it did exist remain coded to it.
Indexes that identify such “retired” parcels must be included in the records system unless provided otherwise by statute.

## Slide 63: Merging adjacent parcels
When two consecutive parcels are merged, the identification of the new parcel shall be next to the identification of the last parcel within the block.

## Slide 65: Working Manual for Urban Cadastral Surveying and Mapping Based on Cadastral Surveying Directive
No.44/2015 Manual No: 26/2016
!

## Slide 66: Geo-database design works
Database issues that are pertinent to the vector datasets need to be handled with knowledge.
Geo-database design works, appropriate projection, local datum, ellipsoid…etc.
Designation has to be properly managed in the geo-databases created prior to getting in to main work of editing.

## Slide 67: Geo-database design works
Here, what should be taken as the basic archiving system is that both the vector and raster data should be archived systematically in such a way that every geo-database, geo-dataset, feature class, image, folder and other vector files should be given a logical name.
This is to mean that a vector data of a given neighborhood, for instance, will be given the name of the specific adjudication site when archived.

## Slide 68: Geo-database design works
Naming the data with the name of a person or other unknown code would not be appropriate and bring about confusion and loss of resource and time sooner or later.

## Slide 69: Sample Geo-database design

## Slide 70: File Geo-database
It is a file folder that holds its dataset files.
Can hold many datasets.
Each data sets consists many feature classes.
Can store up to 1 TB data.
Cross platform
cannot support versioning.
single users with smaller group.
Compressed and encrypted for security purpose.

## Slide 71: Sample spatial data archiving system

## Slide 73: Examination and verification of vector data (1/4)
As the assigned surveyor/s or mapping staff begin managing the vector data by, of course, draping the vector file over the image, the first task would be naturally to examine how well the vector parcels overlap with similar features on the image.
However there may be a slight shifting since line maps was made using stereoscopic view in 3D environment and unlike the 2D desktop the line map were displayed.

## Slide 74: Examination and verification of vector data (2/4)
Regarding the existing vector file, there could be some pocket areas having slight shifts, gaps and overlaps that need editing by applying both desktop GIS/Mapping and ground survey data collection and its integration with the vector data.
Vector data shall be checked for its completeness using Topology rule i.e.
Point line, and polygon topology rules will be applied.

## Slide 75: Examination and verification of vector data (3/4)
Examination of the vector-image fitting and verification should be conducted at then City/town Block level.
Data verification is both manageable and helps easy identification of problem areas and accomplished works. The city/town block level map for vector image verification shall be done based on procedures stipulated at Adjudication Regulation 324 /2014 at Art 9.

## Slide 76: Examination and verification of vector data (4/4)
Neighborhood-level maps should be prepared when field verification is planned. These maps will be used by both the demarcation staff and the surveyors.

## Slide 77: Sample Neighborhood level map for field verification

## Slide 78: Examination and verification of vector data – cases???
If a parcel or a group of parcels on the vector file are well- captured during digitization, these parcels still need to be verified on the ground by the boundary demarcation team and approved by Cadastre officer.

## Slide 79: Examination and verification of vector data – case 1
If the data brought by the demarcation team confirms the accuracy seen on the parcel data of cadastral base map, then that parcel or a group of parcels will be passed on to adjudication.

## Slide 80: Examination and verification of vector data – case 2
If the data brought by the demarcation team indicates the need for slight modifications, then the parcel or the group of parcels will be modified
  Splitting
  Merging
  moving vertices
  …etc tasks on parcel vector
in office using GIS editing techniques as will be practiced during the training (see next slides)

## Slide 81: Feature splitting.
If certain parcel on the vector data becomes more than one, then the office surveyors shall confirm with the reality on the ground by sub dividing. Steps:
Use Editor tool in Arc Map and select the feature class you want to edit.

## Slide 82: Feature splitting
Right-click the selected parcels and click construct from parent.
Use cut polygon tools to divide the selected parcel with straight segment.
The size of the subdivided parcels shall be based on the parcel standard of the area.

## Slide 83: Feature splitting
Keeping the above case in the office, there may also be conditions for Ground Survey Work. Whenever there is a total shape mismatch1 between the vector parcel and the feature on the ortho-photo or if there is a total absence of a vector parcel feature from the vector dataset, the following procedures should be followed in collecting the parcel data.
Steps
  The demarcation team verifies the existence of the parcel or a group of parcels on the ground and collects the relevant data.
  Based on the data collected by the demarcation team, a field survey work is planned and conducted.

## Slide 89: Basic of Onscreen Digitization
Cadastral Features Editing
(topics of upcoming sessions)

## Slide 90: Basic of Onscreen Digitization
City (GDB)
  Kebele
  Ketena
  Sefer
  Block
  Parcels
Orthophoto
 Database structure created
Kebele Boundary imported
Survey data imported
Notes: City (GDB)
  Kebele
  Ketena
  Sefer
  Block
  Parcels

## Slide 91: Advanced Cadastral Features Editing
Auto-complete Polygon
Snapping
Reshape
Vertex edit
Split & Merge

## Slide 92: Topology
Avoid topological errors

## Slide 93
+

## Slide 94
+

## Slide 95
+

## Slide 96: Topological errors
Undershoot
Overshoot
Dangling nodes

## Slide 97
+

## Slide 99: Topology rules

## Slide 101
+

## Slide 102: Sample geo-database template

## Slide 107: Modify the geodatabase
City Level
Kebele Level

## Slide 108: Rules
One section has
  Five Neighborhoods
One Neighborhood has
  200 and below parcels
In One section there are
  1000 and below parcels

## Slide 109: Rules As a national standard the UPIC shall hold the following form